## Slide 1: Chapter 7 – Testing

## Slide 2: Motivation
Development is accompanied by “bugs.”
Catching bugs early saves money
  The further a bug progresses the more impact it has on the system
    A bug fix requires all related modules to be retested.
    A bug fix may require redesigning related modules.
  For example
    PCB design flaw
    VLSI layout error
    Subtle coding flaw
Testing doesn’t remove bugs, it just makes it less likely they exist.

## Slide 3: Learning Objectives
By the end of this chapter, you should:
Understand the concepts of black box tests, white box tests, observability, and controllability.
Understand the principles of debugging.
Understand when a unit test is used and how it is constructed.
Understand when an integration test is used and how it is constructed.
Understand when an acceptance test is used and how it is constructed.

## Slide 4: 7.1 Testing Principles
Testing proceeds with design process
  Write tests while designing modules,
  Perform tests while implementing modules
The Test-Vee illustrates this process

## Slide 5: Testing
Quality design documents
  Requires you to reason about system behavior
  Gives you design clear goals
  Look at your system from the tester’s perspective
How should we perform testing?
  Tradeoff
    Apply every possible input, or
    Apply selected inputs which might yield errors
  Test should be chosen to increase likelihood of finding an error.

## Slide 6: Why Test Cases?
Test cases define exactly what the module must do.
Testing prevents feature creep, since the development of a module is complete when its test is passed.
Test cases motivate developers by providing immediate feedback.
Test cases force designers to think about extreme cases.
Test cases are a form of documentation.
Test cases force the designer to consider the design of the module before building it.

## Slide 7: Types of test
Black box
  No knowledge of internal organization
  Only access input and outputs
  Change inputs and observe outputs
White box
  Knowledge of internal organization
  Might have expectation of fault model
  Create test instance which reveal physical or logical errors

## Slide 8: Testable
Testable – failure of a component can
  Quickly detected
  Quickly located
Controllability
  When any node of the system can be set to a desired value
  Black box has no controllability
Observability
  When any node of the system can be measured.
  Black box has low observability

## Slide 9: Stub
Stub
  A placeholder for future functionality
  A device which mimics subsystem
    Simulates input or monitors outputs
    For a unit under test (UUT)
    Insure good behavior
      before wreaking havoc on the rest of the system
For example
  A function generator for a audio input
  A printf() instead of a file write
  DIP switch instead of a bus connection

## Slide 10: Stub example

## Slide 11: Test case properties
Accurate - The test should check what it is supposed to and exercise an area of intent.
Economical - The test should be performed in a minimal number of steps.
Limited in complexity - Tests should consist of a moderate number (10-15) of steps.
Repeatable - The test should be able to be performed and repeated by another person.
Appropriate - The complexity of the test should be such that it is able to be performed by other individuals who are assigned the testing task.
Traceable - The test should verify a specific requirement.
Self cleaning - The system should return to the pre-test state after the test is complete.

## Slide 12: 7.2 Constructing Tests
Debugging
Bohrbugs
  Bohrbugs are reliable bugs
  The error is always in the same place
  An electrons having a definite position
  Solution = set a good trap
Heisenbugs
  Innocuous changes of input yield buggy behavior
  May not be reproducible
  They seemingly move around within a system
  Electron is elusive density function
  Solution = think outside the box

## Slide 13: Debugging process
Observe the problem under different operating conditions
Form a hypothesis as to what the potential problem is
Conduct experiments to confirm or eliminate the hypothesized source of the problem
Repeat until the problem is eliminated

## Slide 14: Common Problems
Check easiest problems first
  You can perform more in a given time
Start at lowest levels of abstraction
  Upper levels rely on lower level
Example
  Is the system powered up?
  Is the testing equipment adjusted properly?
  Are the bus lines being correctly manipulated?
  Have you initialized the system?
  Are you printing out the right variable/type?

## Slide 15: Unit Testing
A unit test is a test of the functionality of a system module in isolation
Should be traceable to the detailed design.
Consists of a set of test cases
Each test case establish that a subsystem performs a single unit of functionality to some specification.
Test cases should be written with the express intent of uncovering undiscovered defects.

## Slide 16: Unit Test – continued
Write unit test during implementation; why?
  White box tests
  Thinking about test situations and conditions may lead the designer to uncover errors before they are ever designed into the system.
  Unit tests need to be written with an understanding of the internal organization of the component, and a system is best understood during its development.

## Slide 17: Unit test - example
if (16 < Celsius Temperature < 32)
Fahrenheit Temperature = ROM[input-16];
else
Fahrenheit Temperature = (9* Celsius Temperature)/5 + 32;
What inputs are used to check the ROM?
What inputs check the conditionals?
Processing path – sequence from A to B
  Test coverage
  Path complete coverage

## Slide 18: Code example
Determine inputs to check all paths
  ACTION1
  ACTION2
  ACTION3
if ((x >= 30) && (x <= 39)) {
ACTION1
} else if ((x >= 80) && (x <= 96)) {
ACTION2
} else if ((x >= 40) && (x <= 56)) {
ACTION 3
}

## Slide 19: Testing Methods
Matrix Test
Automated Scripts Tests
Step-by-step Test
Note: these can be applied to any level of test: unit, integration, acceptance, etc.

## Slide 20: Matrix Test
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  |  | 
 | Test Case Name: |  | ADC function test |  |  | Test ID #: |  |  | ADC-FT-01
 | Description: |  | Verify conversion range and clock frequency. Output goes to 0 in presence of null clock. |  |  | Type: |  |  |  white box  black box
Tester Information |  |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  | Date: |  |  | 
 | Hardware Ver: |  | 1.0 |  |  | Time: |  |  | 
 | Setup: |  | Isolate the ADC from the system by removing configuration jumpers. |  |  |  |  |  | 
Test | VT | Clock |  | Expected output |  | Pass | Fail | N/A | Comments
 |  |  |  | Decimal | Hexadecimal |  |  |  | 
1 | 0.0V | 10kHz |  | 0 | 0x000 |  |  |  | 
5 | 2.0V | 0Hz |  | 0 | 0x000 |  |  |  | 
 | Overall test result: |  |  |  |  |  |  |  | 

## Slide 21: Step-by-Step Test
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Finite State Machine Path Test #1 |  |  |  |  | Test ID #: | FSM-Path-01
 | Description: | Simulate insertion of money with a mix of nickels and dimes. Verifies FSM, outputs candy in response to a total deposit of $0.30. |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | 1.0 |  |  |  |  | Time: | 
 | Setup: | Make sure that the system was reset sometime prior and is in state $0.00. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Strobe Nickel | State should go to $0.05 |  |  |  |  |  | 
2 | Strobe Dime | State should go to $0.15 |  |  |  |  |  | 
3 | Wait | State should remain $0.15 |  |  |  |  |  | 
4 | Strobe Nickel | State should go to $0.20 |  |  |  |  |  | 
5 | Strobe Dime | State should go to $0.25 |  |  |  |  |  | 
6 | Nothing | State should go to $0.00 |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 22: Integration Testing
Write integration test during level 1 design
  Help insure requirements are being met.
  Help to firm-up design
  Requires the designer think about the expected behavior of the subsystems.
  Requires designer to think about extreme behaviors of subsystems.

## Slide 23: Write the Integration Test
What are the different paths of execution through the system?
Are all modules exercised at least once during integration testing?
Have all the interface signals been tested?
Have all the interface modes been exercised?
Does the system process information at the required rate and met timing requirements?

## Slide 24: Acceptance Testing
Might be formal legal document
Written along with requirements
Traceable to engineering requirements
Identifies
  Scope – how much of the system is tested?
  Level – how deep will testing be performed?

## Slide 25: 7.3 Application: Autonomous Robot
Autonomous navigating robot
Engineering requirements
  The robot’s center must stay within 12 to 18 centimeters of the wall over 90% of the course, while traveling parallel to a wall over a 3 meter course.
  The robot’s heading should never deviate no more than 10 degrees from the wall’s axis, while traveling parallel to a straight wall over a 3 meter course.

## Slide 26: Robot Acceptance Test
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Robot acceptance test #1 |  |  |  |  | Test ID #: | Robot-AT-01
 | Description: | Checks the engineering requirement: The robot’s center must stay within 12 to 18 centimeters of the wall over 90% of the course, while traveling parallel to a wall over a 3 meter course. |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | Robot 1.0 |  |  |  |  | Time: | 
 | Setup: | Completed robot should be fully charged and placed on 3 meter test track. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Write a program to monitor the robots position from the wall. | Program should be statically tested to verify accuracy. Should sample wall at a sufficient rate depending on speed. |  |  |  |  |  | 
2 | Put robot on test track, run test, and download data. | The robot should travel down the entire length of the test track and then stop. |  |  |  |  |  | 
3 | Plot test data in a spreadsheet program. | Plot of position vs. time should be within 12 – 18 cm 90% of the time. |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 27: Example: Robot architecture

## Slide 28: Some Integration Test Possibilities
MCU + motors + bridge + switches
Chassis + digital compass + MCU + motors + bridge +LCD
Chassis + range finder + MCU + motors + bridge

## Slide 29: A step-by-step integration test
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Robot integration test #1 |  |  |  |  | Test ID #: | Robot-IT-01
 | Description: | Checks interaction of DC motors on the magnetic compass. |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | Robot 1.0 |  |  |  |  | Time: | 
 | Setup: | A wooden turn-table should be placed on top of the cardinal direction map. This map should be aligned with a magnetic compass. There should be no metal present while the alignment is being performed. Next, the partially assembled robot should be placed on the turn-table. The MCU should be connected to a terminal to observe and record data. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Write program to spool compass readings while simultaneously driving motors. | Program should be statically tested to verify accuracy. Should sample compass at a sufficient rate depending on speed. |  |  |  |  |  | 
2 | Run acceptance test | Test program should prompt user to turn the robot to an orientation and then spin the motors will then spin up and down. |  |  |  |  |  | 
3 | Plot spooled data in spreadsheet program. | Plots should be analyzed to see if compass deviated any more than 10 degrees from set point. |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 30: Unit testing possibilities
MCU (hardware)
LCD
Switches
Compass
Range finder
H-bridge
Motors
Chassis
MCU (software)

## Slide 31: Unit Test: The Digital Compass
Module | Digital Compass – Geosensor version 2.3
Inputs | Earth’s magnetic field: An orientated field of magnetic force beginning and ending at the earth’s magnetic poles. SClk – Clock signal to clock data through the module. Maximum Frequency is 10Mhz. SDIn – Serial data input to send data into the compass module. Date is valid on positive SClk edges.
Outputs | SDOut – Serial data output from the compass module. Data is valid on negative clock edges.
Functionality | Senses the earth’s magnetic field and determines the orientation of the compass with respect to the field. This orientation is stored in an internal register and can be retrieved through the SPI interface.
Test | Comp-UT-01

## Slide 32: Unit test: compass (matrix)
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Compass unit test #1 |  |  |  |  | Test ID #: | Comp-UT-01
 | Description: | Checks that the compass returns correct angular measurements to the MCU. Test program is in ./test/compass_unit_test_1.c |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | Compass Module - Geosensor version 2.3 |  |  |  |  | Time: | 
 | Setup: | Compass module should be wired to the MCU through the SPI interface pins. The MCU should be connected to an RS232 terminal through its SCI interface. The terminal should be configured to run at 9600 baud. Cardinal directions map should be aligned using the magnetic compass. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Compile compass.c in /test directory | IDE should generate no warnings or errors. |  |  |  |  |  | 
2 | Download | MCU should report “download successful” |  |  |  |  |  | 
3 | Execute | MCU should display compass splash screen on terminal interface. |  |  |  |  |  | 
4 | Orientate compass to 0 degrees. | Terminal interface should display 0 degrees +/- 10 degrees. |  |  |  |  |  | 
5 | Orientate compass to 30 degrees. | Terminal interface should display 30 degrees +/- 10 degrees. |  |  |  |  |  | 
6 | Orientate compass to 45 degrees. | Terminal interface should display 45 degrees +/- 10 degrees. |  |  |  |  |  | 
… | … | … |  |  |  |  |  | 
12 | Orientate compass to 315degrees. | Terminal interface should display 315 degrees +/- 10 degrees. |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 33: 7.4 Guidance
Reasons to develop and conduct tests
Testing reduces the number of bugs in existing and new features.
Tests are good documentation.
Tests improve design.
Tests allow you to refactor.
Tests constrain features.
Tests defend against other designers.
Testing is fun.
Testing forces you to slow down and think.
Testing makes development faster.
Tests reduce fear.

## Slide 34: 7.5 Summary
Testing helps to ensure proper operation of system.
Types of Testing
  Block box
  White box
  Unit Testing
  Integration Testing
  Acceptance Testing
  Matrix tests
  Step-by-step test
  Automated tests