## Slide 1: Appendix B – Decision Making with AHP

## Slide 2: Motivation
Decision making is a hallmark of design.
Often faced with multiple alternatives and criteria against which decision must be made.
Analytical Hierarchy Process (AHP) is a well-known an intutive method.
Making good decisions is a crucial skill at every level.—Peter Drucker

## Slide 3: A Decision Matrix
 |  | Alternative 1 | Alternative 2 |  | Alternative n
Criteria 1 |  | 11 | 12 |  | 1n
Criteria 2 |  | 21 | 22 |  | 2n
Criteria m |  | m1 | m2 |  | mn
Score |  |  |  |  | 

## Slide 4: Steps of AHP
Determine the selection criteria.
Determine the criteria weightings.
Identify and rate alternatives relative to the criteria.
Compute scores for the alternatives.
Review the decision.

## Slide 5: B.1 Apply AHP for Car Purchase
Decision = select car to purchase
Step 1: Determine Criteria
  Purchase cost
  Safety
  Design styling
  Brand-name recognition

## Slide 6: Step 2 – Select Weighings
Need to select weightings of criteria (relative importance)
Number of ways – one is pairwise comparison
Compare each criterion to all others with following scale
1 = equal, 3 = moderate, 5 = strong, 7 = very strong, 9 = extreme.

## Slide 7: Step 2 (paired comparison)
 | Purchase cost | Safety | Design | Brand-name
Purchase cost | 1 | 1 | 3 | 7
Safety | 1 | 1 | 5 | 9
Design | 1/3 | 1/5 | 1 | 3
Brand-name | 1/7 | 1/9 | 1/3 | 1

## Slide 8: Paired comparison w/reduced bias
 | Purchase cost | Safety | Design | Brand-name | Geometric Mean | Weights
Purchase cost | 1 | 1 | 3 | 7 | 2.1 | 0.37
Safety | 1 | 1 | 5 | 9 | 2.6 | 0.46
Design | 1/3 | 1/5 | 1 | 3 | 0.7 | 0.12
Brand-name | 1/7 | 1/9 | 1/3 | 1 | 0.3 | 0.05

## Slide 9: Step 3: Identify Alternatives & Rate
Alternatives are determined to be:
Honda CRV
Hyundai Tucson
Toyota RAV4
All 2006 model year

## Slide 10: Rate relative to cost
The vehicle costs are $21,026 (Honda), $18,183 (Hyundai), and $21,989 (Toyota).
Direct quantitative comparison possible
11 = 0.86, 12= 1, and 13= 0.83
Normalized to 11 = 0.32, 12 = 0.37, and 13 = 0.31

## Slide 11: Rate relative to safety
Use metric from US National Highway Transportation Safety Association – 5 star rating system.
Produces the following normalized ratings: 21 = 0.34, 22 = 0.34, and 23 = 0.32

## Slide 12: Rate relative to design styling
This is subjective => need to quantify subjective opinion
Use paired comparison to do so, with same scale as before
 | Honda CRV | Hyundai | RAV4 | Design Rating
Honda CRV | 1 | 1/3 | 1/5 | 0.11
Hyundai Tucson | 3 | 1 | ½ | 0.31
RAV4 | 5 | 2 | 1 | 0.58

## Slide 13: Rate relative to brand name
Again, use paired comparison to quantify subjective ratings
 | Honda CRV | Hyundai Tucson | RAV4 | Brand-name rating
Honda CRV | 1 | 4 | 1 | 0.44
Hyundai Tucson | ¼ | 1 | ¼ | 0.12
RAV4 | 1 | 4 | 1 | 0.44

## Slide 14: Step 4: Compute Scores for Alternatives
 |  | Honda CR-V | Hyundai Tucson | RAV4
Cost | 0.37 | 0.32 | 0.37 | 0.31
Safety | 0.46 | 0.34 | 0.34 | 0.32
Design styling | 0.12 | 0.11 | 0.31 | 0.58
Brand-name | 0.05 | 0.44 | 0.12 | 0.44
Score |  | 0.31 | 0.34 | 0.35

## Slide 15: Step 5: Review the Decision
Scores are close, thus all are pretty good choices (based on criteria).
Toyota RAV4 has the highest
Toyota beats the Hyundai, based on design styling and brand name recognition.
If cost and safety were given greater weight, the Hyundai would beat the Toyota.

## Slide 16: B.2 Hierarichical Decision Criteria
 |  | Honda CR-V | Hyundai Tucson | RAV4
Purchase Cost | 0.33 | 0.32 | 0.37 | 0.31
Operating Cost | 0.11 | 0.34 | 0.32 | 0.33
Fuel | 0.67 | 0.33 | 0.32 | 0.35
Insurance | 0.33 | 0.36 | 0.34 | 0.30
Safety | 0.40 | 0.34 | 0.34 | 0.32
Design Styling | 0.12 | 0.20 | 0.40 | 0.40
Interior | 0.60 | 0.20 | 0.40 | 0.40
Exterior | 0.40 | 0.20 | 0.40 | 0.40
Brand-name | 0.04 | 0.44 | 0.12 | 0.44
Score |  | 0.32 | 0.35 | 0.33

## Slide 17: B.3 Summary
Ideally, criteria are selected prior to alternatives.
Criterion weights can be selected a number of ways. Paired comparison is one way, and it can be used to reduce bias.
Sum of weight should be normalized to 1.
If quantitative data is availble for ratings of alternatives relative to criteria, use it.
Otherwise, must use semi-qualitative approach, such as paired comparison.
Review the final result critically.