## Slide 1: Chapter 3 – The Requirements Specification

## Slide 2: Motivation – A Real Job Advertisement
Product Design Engineer (Electrical)
Duties and responsibilities of the position include: designing and developing new products and modifying/enhancing existing products to meet customer specification. This will be accomplished by communicating with internal and external customers to identify requirements; coordinating and implementing processes with manufacturing engineering based upon customer needs; and maintaining and/or creating supporting documentation

## Slide 3: What came first?

## Slide 4: Chapter 3 – Learning Objectives
By the end of this chapter, you should:
Understand the properties of an engineering requirement and know how to develop well-formed requirements that meet the properties.
Be familiar with engineering requirements that are commonly specified in electrical and computer systems.
Understand the properties of the complete requirements specification, as well as knowing the steps to develop one.
Be able to conduct advanced requirements analysis to identify tradeoffs.

## Slide 5: 3.1 Overview of Process [IEEE-STD 1233]

## Slide 6: Definitions
Marketing Requirement
Engineering Requirement
Requirements Specification

## Slide 7
3.2 Engineering Requirements

## Slide 8: Engineering Requirement Properties
1) Abstract
2) Verifiable

## Slide 9: Engineering Requirement Properties
3) Unambiguous
4) Traceable

## Slide 10: Example
Does the following requirement meet the four desirable properties? (abstract, unambiguous, verifiable, traceable)
“The audio amplifier will have a total harmonic distortion that is less than 2%.”

## Slide 11: Example
Does the following requirement meet the four desirable properties? (abstract, verifiable, unambiguous, traceable)
“The robot must have an average forward speed of 0.5 feet/sec, a top speed of at least one foot/sec, and the ability to accelerate from standstill to the average speed in under one second.”

## Slide 12: Example
Does the following requirement meet the four desirable properties? (abstract, unambiguous, verifiable, traceable)
“The robot must employ IR sensors to sense its external environment and navigate autonomously with a battery life of one hour.”

## Slide 13: Example
Does the following requirement meet the four desirable properties? (abstract, unambiguous, verifiable, traceable)
“The system shall be easy to use by an intelligent 12 year old.”

## Slide 14: A Fifth Property - Realism
IMPORTANT – Your requirements for your project must also be REALISTIC.
=> You need to demonstrate that the target you have selected is technically feasible.
How are you going to do this?

## Slide 15: Constraints
Constraint = design decision imposed by the environment or a stakeholder that impacts or limits the design. (see the original overview diagram).
Example contraint: The system must use a PIC18F52 microcontroller to implement processing functions.

## Slide 16: Standards
A standard is what?
Question is, what standards are relevant to your project and how do you use them?
Different levels of usage
  User
  Implementation
  Developer
Types: safety, testing, reliability, communication, data, documentation, design, …

## Slide 17: Identifying Engineering Requirements
Structured workshops and brainstorming
Interviews and surveys
Observation of processes and devices in use
Benchmarking and market analysis
Prototyping and simulation
Research survey

## Slide 18: Engineering Requirement Examples
Need to know what type of requirement to select for a given system.
These are but EXAMPLES – you must determine the correct ones for your system!
Hint: don’t just try to copy and paste them.

## Slide 19: Engineering Requirement Examples
Performance
The system should detect 90% of all human faces in an image.
The amplifier will have a total harmonic distortion less than 1%.
Reliability & Availability
The system will have a reliability of 95% in five years.
The system will be operational from 4AM to 10PM, 365 days a year.

## Slide 20: Engineering Requirement Examples
Energy
The system will operate for a minimum of three hours without needing
Environmental
The system should be able to operate in the temperature range of 0°C to 75°C.
The system must be waterproof and operate while submersed in water.
to be recharged.
Many more examples in the book.

## Slide 21
3.3 The Requirements Specification

## Slide 22: Requirements Specification
Definition

## Slide 23: Properties of the Requirements Specification
Normalized/Orthogonal
Complete Set

## Slide 24: Properties of the Requirements Specification
Consistent
Bounded

## Slide 25: Validation
Validation =

## Slide 26: How do you VALIDATE requirements?
Ask the customer if the requirements meet their needs.
Usually done in teams.
For each engineering requirement
  Traceable?
  Verifiable?
  Realistic & technical feasible?
For the complete Requirements Specification
  Orthogonal?
  Complete?
  Consistent?

## Slide 27: Mapping (Audio Amplifier)
Marketing Requirement
Should have excellent sound quality.
Engineering Requirement
Total harmonic distortion should be ≤ 1%.
Justification
Based upon competitive benchmarking and existing amplifier technology. Class A, B, and AB amplifiers are able to obtain this level of THD.

## Slide 28: Mapping (Audio Amplifier)
Marketing Requirement
Should have excellent sound quality.
Engineering Requirement
Signal to Noise Ratio should be exceed 120dB.
Justification

## Slide 29: More Mapping, cont’d
Marketing Requirement
Should have high output power.
Engineering Requirement
Should be able to sustain an output power that averages  35 watts with a peak value of  70 watts.
Justification
This power range provides more than adequate sound throughout the automobile compartment and is competitive in this price range.

## Slide 30: Mapping, cont’d
Marketing Requirement
Should be easy to install.
Engineering Requirement
Average installation time for the power and audio connections should not exceed 5 minutes.
Justification
Past trials using standard audio and power jacks demonstrate that this is a reasonable installation time.

## Slide 31: 3.4 Case Study: Car Audio Amp
Marketing Requirements | Engineering Requirements | Justification
1, 2, 4 | The total harmonic distortion should be <0.1%. | Based upon competitive benchmarking and existing amplifier technology. Class A, B, and AB amplifiers are able to obtain this level of THD.
1–4 | Should be able to sustain an output power that averages  35 watts with a peak value of  70 watts. | This power range provides more than adequate sound throughout the automobile compartment. It is a sustainable output power for projected amplifier complexity.
2, 4 | Should have an efficiency () >40 %. | Achievable with several different classes of power amplifiers.
3 | Average installation time for the power and audio connections should not exceed 5 minutes. | Past trials using standard audio and power jacks demonstrate that this is a reasonable installation time.

## Slide 32: Case Study, cont’d
1–4 | The dimensions should not exceed 6” x 8”x 3”. | Fits under a typical car seat. Prior models and estimates show that all components should fit within this package size.
1–4 | Production cost should not exceed $100. | This is based upon competitive market analysis and previous system designs.
Marketing Requirements The system should have excellent sound quality. The system should have high output power. The system should be easy to install. The system should have low cost. |  | 

## Slide 33: Case Study: iPod Hands Free
Marketing Requirements | Engineering Requirements | Justification
4, 6 | System will implement nine voice command functions ( menu, play/pause, previous, next, up, down, left, right and select) and respond appropriately according to each command. | These are the basic nine commands that are used to control an iPod and will provide all functionality needed.
1, 3, 4, 7 | The time to respond to voice commands and provide audio feedback should not exceed 3 seconds. | The system needs to provide convenient use by responding to the user inputs within a short time period. Based on research it was determined that the response time for the iPod is less than 1 second and an average voice recognition system requires 2 seconds to recognize commands.
4, 6 | The accuracy of the system in accepting voice commands will be between 95% and 98%. | Research demonstrates that this is a typical accuracy of voice recognition chips. Speaker independent systems can achieve 95% and speaker-dependent up to 98%.

## Slide 34: Case Study, cont’d
5, 6 | The system should be able to operate from a 12 V source and will draw a maximum of 150 mA. | The automobile provides 12V DC. A current draw budget estimate was developed with potential components and 150mA was an upper limit of current estimated.
5, 6, 7 | The dimensions of the prototype should not exceed 6” x 4” x 1.5”. | This system must be able to fit in a car compartment, somewhere between the seats. Estimate is based upon a size budget calculation using typical parts.
Marketing Requirements Should not minimize or slow down the functional quality of the iPod. User should be able to search for songs and artists and receive feedback on selection. System should provide clear understandable speech. System should be able to understand voice commands from user. Should be able to fit and operate in an automobile. Should be easy to use. Should be portable. |  | 

## Slide 35
3.5 Advanced Requirements Analysis

## Slide 36: Engineering-Marketing Matrix
 |  | THD | Output Power | , Efficiency | Install Time | Dimensions | Cost
 |  | - | + | + | - | - | -
1) Sound Quality | + |  |  |  |  |  | 
2) High Power | + |  |  |  |  |  | 
3) Install Ease | + |  |  |  |  |  | 
4) Cost | - |  |  |  |  |  | 

## Slide 37: Engineering Tradeoff Matrix
 |  | THD | Output Power | , Efficiency | Install Time | Dimensions | Cost
 |  | - | + | + | - | - | -
THD | - |  |  |  |  |  | 
Output Power | + |  |  |  |  |  | 
, Efficiency | + |  |  |  |  |  | 
Install Time | - |  |  |  |  |  | 
Dimensions | - |  |  |  |  |  | 
Cost | - |  |  |  |  |  | 

## Slide 38: Competitive Benchmarks
 | Apex Audio | Monster Amps | Our Design
THD | 0.05% | 0.15% | 0.1%
Power | 30W | 50W | 35W
Efficiency | 70% | 30% | 40%
Cost | $250 | $120 | $100
38

## Slide 39: 3.6 Project Application: The Requirements Specification
A complete requirements document will contain:
Needs, Objectives, and Background (See Chapter 2).
Requirements.
  marketing requirements
  engineering requirements
    Should be abstract, verifiable, and traceable
    Some maybe constraints
    Some may be standards
  Advanced analysis
    Engineering-marketing tradeoffs
    Engineering-engineering tradeoffs
    Benchmarks

## Slide 40: 3.7 Summary
Properties of engineering requirements
Examples of engineering requirements
Properties of the Requirements Specification
Advanced Requirements Analysis
  Tradeoff matrices
  Benchmarks