## Slide 1: Chapter 4 – Concept Generation & Evaluation

## Slide 2: Motivation
Creativity is part of being an engineer.
We often start with a single solution to a problem and then pursue it as the only possibility.
Need to be creative and generate a variety possible designs.
Need to be able to evaluate different designs.
Systematic generation
BE ABLE TO DEFEND YOUR DESIGN!
Companies want to employ innovative engineers.
Develop your engineering judgment.

## Slide 3: Learning Objectives
By the end of this chapter, you should:
Understand the importance of creativity, innovation, concept generation, and critical evaluation in engineering design.
Be familiar with barriers that hinder creativity.
Be able to apply strategies and formal methods to generate concepts.
Be able to apply techniques for the evaluation of design concepts.

## Slide 4: 4.1 Creativity (Brainteaser)
Think of this as a shovel with a coin on the shovel. The problem is to move two of the “toothpicks” so that the coin is no longer in the shovel, but you still have a shovel.
Notes: | |
|_____|
|
* |
Slide the top of the shovel over by half. People tend to put an artificial constraint and only want to move a toothpick completely. In this case, you only slide it to the right.

## Slide 5: Barriers to Creativity
Perceptual
Emotional
Cultural and Environmental
Intellectual and Expressive
Notes: Perceptual blocks
Emotional blocks
Cultural blocks
Intellectual and expressive blocks

## Slide 6: Perceptual Blocks

## Slide 7: Vertical and Lateral Thinking
“A body is discovered in a park in Chicago in the middle of summer. It has a fractured skull and many other broken bones, but the cause of death was hypothermia.”
Think of the TV show CSI – Crime Scene Investigation. Generate as many solutions as possible to the following scenarios. The idea is to see the problem from a variety of different viewpoints and generate plausible scenarios. You have insufficient information and should examine your assumptions.

## Slide 8: Vertical and Lateral Thinking
Vertical thinking is?
Lateral thinking is?

## Slide 9: Strategies for Creativity
Have a questioning attitude
Practice being creative
Suspend judgment
All incubation time
Think like a beginner

## Slide 10: SCAMPER
SCAMPER
Substitute
Combine
Adapt
Modify
Put to other use
Eliminate
Rearrange or Reverse

## Slide 11: 4.2 Concept Generation
Search Externally
Literature review
Search and review existing products
Benchmark similar products
Interview experts
Search Internally
Brainstorming/brainwriting
Nominal Group Technique
Concept Table/Fans

## Slide 12: Brainstorming
Rules for group brainstorming
No evaluation or judgment of ideas permitted.
Encourage wild ideas.
Focus on quantity, not quality (can always toss later!)
Build upon, combine, or modify the ideas of others (SCAMPER).
Record all ideas.

## Slide 13: Morphology: Personal Computing
User Interface | Display | Connectivity & Expansion | Power | Size
Keyboard | CRT | Serial & parallel | Battery | Hand-held, Fits in pocket
Touchpad | Flat Panel | USB | AC Power | Notebook size
Handwriting Recognition | Plasma | Wireless Ethernet | Solar Power | Wearable
Video | Heads-up display | Wired Ethernet | Fuel Cell | Credit card size
Voice | LCD | PCMCIA | Thermal transfer | Flexible in shape
 |  | Modem / Telephone |  | 

## Slide 14: Concept Fan

## Slide 15: 4.3 Concept Evaluation
Decision Methods (some of them)
Strength & Weakness Analysis
Analytical Hierarchy Process (Decision Matrix)
Pugh Concept Selection

## Slide 16: Strength & Weakness Analysis
Identify and list strengths and weaknesses of each concept.
To make more analytical, assign subjective weights to strengths and weaknesses (plus and minus factors) and sum them.

## Slide 17: AHP (Decision Matrix)
 |  | Design Option 1 | Design Option 2 |  | Design Option n
Criteria 1 |  | 11 | 12 |  | 1n
Criteria 2 |  | 21 | 22 |  | 2n
Criteria m |  | m1 | m2 |  | mn
Score |  |  |  |  | 

## Slide 18: Decision Matrix: Steps
Step 1: Determine the selection criteria
Step 2: Select the criteria weightings
Step 3: Identify and rate alternatives relative to the criteria
Step 4: Compute the scores
Step 5: Review the decision
  You can use all the quantitative data you can get, but you still have to distrust it and use your own intelligence and judgment.—Alvin Toffler

## Slide 19: Example: Quantitative Decision
Select a current source circuit for current measurement

## Slide 20: Step 1: Select the Criteria
In this case they are given as
Accuracy
Cost
Size
Availability

## Slide 21: Step 2: Select the Weighting Factors
These are computed based upon the results of the pairwise comparison – given in the problem.
Be sure to normalize the final values.

## Slide 22: Step 3: Compute Design Ratings
They need to be computed for the following
Accuracy
Cost
Size
Availability

## Slide 23: Step 4: Compute the Scores
 |  | Single BJT | Op Amp | Current Mirror
Accuracy | 0.42 |  |  | 
Cost | 0.12 |  |  | 
Size | 0.12 |  |  | 
Availability | 0.34 |  |  | 
Score |  |  |  | 
23

## Slide 24: Pugh Concept Selection
Select the comparison criteria
Determine weights for the criteria
Determine the concepts
Select baseline concept, initially believed best
Compare other concepts to baseline:
  +1 better than, 0 equal to, -1 worse than.
Compute weighted score for concepts, not including the baseline.
Examine concepts: retain, update, or drop. Synthesize best elements of others where possible.
Update table & iterate until best concept emerges.

## Slide 25: Pugh Concept Table
 |  | Option 1 (Reference) | Option 2 | Option 3 | Option 4
Criteria 1 | 4 | - | 0 | 0 | +1
Criteria 2 | 5 | - | +1 | -1 | 0
Criteria 3 | 2 | - | -1 | 0 | +1
Criteria 4 | 1 | - | +1 | +1 | -1
Score |  | - | 4 | -4 | 5
Continue? |  | Combine | Yes | No | Combine

## Slide 26: 4.4 Project Application
Identify different design alternatives (see also Chapters 5 and 6).
  Search externally
  Brainstorming sessions.
  Nominal Group Technique
  Morphology (Concept Tables and Fans)
  SCAMPER
Identify leading concept and justify
  Strength & Weaknesses Analysis
  Decision Matrices
  Pugh Concept Selection

## Slide 27: 4.5 Summary
Open your mind to creativity
  Innovation is important
  There are strategies to apply
Apply Methods of Concept Generation
  Search externally: Patents, research, experts
  Search internally: SCAMPER, Morph Charts, Concept Fans, Brainstorming, Nominal Group Technique
Evaluate Concepts Critically
  Strengths/Weaknesses
  Decision Matrices
  Pugh Concept Selection

## Slide 28: In-class Exercise - Step 1
Get into teams
Use brain writing 6-3-5 to develop as many solutions as possible to the following problem.
Each team needs to have 5-10 ideas to present to the class. Ideas need to be written down.
“Legislation was passed to allow handguns in the cockpits of passenger airliners to prevent hijacking. Develop concepts that prevent anyone other than the pilot from using the handgun.
15 minutes

## Slide 29: Step #2
Identify 4-6 criteria against which your solutions should be judged.
Write down the final criteria.
5 minutes

## Slide 30: Step 3- Pugh Concept Selection
As a team, apply Pugh concept selection to select an idea relative to the criteria you have selected.
Turn in copies of the progressive selection matrices.
20 minutes